CORRIGENDUM No: 1

to the

# ANNEX II + III: TECHNICAL SPECIFICATIONS + TECHNICAL OFFER

Publication Ref: RORS 27- TD 06

# Subject: Purchase of vehicles

# Location: Serbia

The TECHNICAL SPECIFICATIONS is corrected or modified as follow:

Point n°2.1: Technical characteristics of Field transport vans

Instead of:

| 2. | Field transport vans suitable for transporting 8+1 firefighters and rescuers and their personal equipment to an emergency, with cargo space | Quantity: 8 pcs |
| --- | --- | --- |
|  | Manufacturer’s name |
|  | Product type, model |
| 2.1. | Technical characteristics |
|  | Diesel engine, EURO 6 |
|  | Minimum power 100 kW |
|  | Manual gearbox min 5+R |
|  | Servo steering |
|  | ABS brakes and ESP and assistance while driving on steep roads |
|  | Wheels size: R16 |
|  | Wheels material: Steel |
|  | Tires: set of winter and set of summer tires |
|  | Vehicle length: minimum 5200 mm |
|  | Number of seats 8+1 |
|  | Number of doors: 4 |
|  | Fuel tank capacity: minimum 70l |
|  | Towing capacity with brakes: min 1000 kg |
|  | Air condition system: automatic / manual for front part and rear part of the cabin |
|  | Colour: White |
|  | Roof gallery for cargo with path |
|  | Ladders for roof gallery loaded on the back door |
|  | Roof gallery and ladders with anti-corrosive protection, made of steel or aluminum |

Read:

| 2. | Field transport vans suitable for transporting 8+1 firefighters and rescuers and their personal equipment to an emergency, with cargo space | Quantity: 8 pcs |
| --- | --- | --- |
|  | Manufacturer’s name |
|  | Product type, model |
| 2.1. | Technical characteristics |
|  | Diesel engine, EURO 6 |
|  | Minimum power 88 kW |
|  | Manual gearbox min 5+R |
|  | Servo steering |
|  | ABS brakes and ESP and assistance while driving on steep roads |
|  | Wheels size: R16 |
|  | Wheels material: Steel |
|  | Tires: set of winter and set of summer tires |
|  | Vehicle length: minimum 5200 mm |
|  | Number of seats 8+1 |
|  | Number of doors: 4 |
|  | Fuel tank capacity: minimum 70l |
|  | Towing capacity with brakes: min 1000 kg |
|  | Air condition system: automatic / manual for front part and rear part of the cabin |
|  | Colour: White |
|  | Roof gallery for cargo with path |
|  | Ladders for roof gallery loaded on the back door |
|  | Roof gallery and ladders with anti-corrosive protection, made of steel or aluminum |

All other terms and conditions of the Technical specification remain unchanged. The above alterations and /or corrections to the Technical specification are integral part of the Technical specification.